## Slide 1: Stateless Best Effort Multicast draft-lx-msr6-rgb-segment-03 draft-chen-pim-be-mrh-00
Huaimo Chen, Donald E. Eastlake, Mike McBride (Futurewei)
Yanhe Fan (Casa Systems)
Gyan Mishra (Verizon)
Yisong Liu (China Mobile
Aijun Wang (China Telecom)
Xufeng Liu (IBM Corporation)
Lei Liu (Fujitsu)
Page 1
MSR6 BoF IETF 114
Yisong Liu (China Mobile
Jingrong Xie, Xuesong Geng (China Telecom)
Mengxiao Chen (New H3C Technologies)

## Slide 2: Brief Description
Page 2
PE2
PE3
PE5
PE4
P1
P2
P3
PE1
PE10
P4
1
10
2
3
5
6
7
8
9
PE6
PE7
PE8
PE9
P5
4
1
CE1
Traffic
Source
link
Loose Hops
Figure 1. Tree from PE1 towards PE2 to PE5
5
4
4
Controller
Egress Join/Leave
P2MP Tree (Egresses)
Ingress (e.g., PE1) encapsulates the packet in a MRH with tree (i.e., egresses of tree)
The packet is transmitted along the shortest IGP pathes to the egresses.
Egress (e.g., PE2) decapsulates the packet in a MRH and sends it to next header process
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Next Header | Hdr Ext Len | Type = TBD | . . . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ +
| ~
+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+
| Tree/Sub-tree (i.e., egresses) encoded |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|<--IPv6 header-->|<--- MRH header --->|
+-----------------+---------------------+------------------------+
| Next Header = | Next Header | (an extension header) |
|60(DoH) or 43(RT)| | IP multicast datagram |
| SA=IPv6 Address | Type = TBD (MRH) | |
| DA=IPv6 Address |Data(Subtree/Egresses| |
+-----------------+---------------------+------------------------+
|<------- MRH ------->|

## Slide 3: Solution 1 Specials: DoH
Page 3
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Next Header | Hdr Ext Len |Option Type=TBD| Option Length |
+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+
| BIFT-id | Rsv | TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Rsv | Ver | BSL | Entropy |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ RGB IPv6
|OAM|Rsv| DSCP | Rsv | Option MRH(DoH)
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ Data for BE
| BitString (first 32 bits) ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ BitString (last 32 bits) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|<--IPv6 header-->|<-- DoH header -->|
+-----------------+------------------+------------------------+
| Next Header = | Next Header | (an extension header) |
| 60 (DoH header) | | IP multicast datagram |
| SA=IPv6 Address | Option Type = | |
| DA=IPv6 Address | TBD (MRH) | |
| | Data (Sub-tree) | |
+-----------------+------------------+------------------------+
|<---- MRH ---->|

## Slide 4: Solution 1 Specials: Forwarding Procedure
Page 4
IF (There is DoH as an IPv6 Extension header and one of the options type is RGB
Lookup BIFT based on the bitstring inside the RGB Option Data
Forward the packet via the matched entry in the BIFT
ELSE IF NH=ICMPv6 or (NH=RGB Extension Header Type and NH of Extension Header=ICMPv6)
Send to CPU.
ELSE ;Ref
Drop the packet.
Ref: An ICMPv6 packet using End.RGB as destination address.

## Slide 5: Solution 2 Specials: Routing Header
Page 5
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Next Header | Hdr Ext Len |RoutingType=TBD|Version| Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|SL(SubtreeLeft/Start)|SE(Subtree End/Size) | Reserved | IPv6
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ MRH (Routing header)
| Sub-tree encoded by Node Indexes, Flexible Bitstrings | for BE
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|<--IPv6 header-->|<-Routing header->|
+-----------------+------------------+------------------------+
| Next Header = | Next Header | (an extension header) |
|43(Routing header| | IP multicast datagram |
| SA=IPv6 Address | Routing Type = | |
| DA=IPv6 Address | TBD (MRH) | |
| | SL, SE, Sub-tree | |
+-----------------+------------------+------------------------+
|<---- MRH ---->|
IPv6 packet with one bitstring sent to P1
DA=P1’s IPv6, SA=PE1’s IPv6
Routing Type=TBD, SL=4, SE=4
sub-tree from P1 towards PE2 to PE5
IP multicast packet
MRH
IPv6 header
Size 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 0 1 2 3 4 5 6 7
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ Encoding indexes
4 |1| 2 | 1 |1|1|1|1|0|0|0|0| of PE2 to PE5 by
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ flexible bitstring
|B|<------- StartIndex ------->|<-S-BitString->|<--BitString-->|

## Slide 6: Solution 2 Specials: Flexible Bitstring and NodeIndex
Page 6
A flexible bitstring has four fields:
1). B flag with value 1, 2). start index (StartIndex), 3). size of bitstring (S-BitString) in bytes and
4). bitstring (BitString), where each bit with value1 indicates a node index equal to StartIndex plus the bit number. Note that the bit number is counted from right to left and from 0.
For example, the indexes of egresses PE2 to PE5 (i.e., PE2, PE3, PE4 and PE5) are encoded by a flexible bitstring (suppose their indexes are 2, 3, 4 and 5 respectively):
B = 1, StartIndex = 2, S-BitString = 1, BitString = 0b11110000 indicating four node indexes 2, 3, 4 and 5.
BitString’s first bit (bit 0) with value 1 indicates the first node index 2 equal to 2 + 0; the BitString’s second bit (bit 1) with value 1 indicates the second node index 3 equal to 2 + 1, and so on.
A NodeIndex field with B = 0 represents a node index directly.
For example, the indexes of egresses PE2 to PE5 are represented by NodeIndex.
Size 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 0 1 2 3 4 5 6 7
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ Encoding indexes
4 |1| 2 | 1 |1|1|1|1|0|0|0|0| of PE2 to PE5 by
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ flexible bitstring
|B|<------- StartIndex ------->|<-S-BitString->|<--BitString-->|
Size 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
8 |0| NodeIndex = 2 (PE2’s Index) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
6 |0| NodeIndex = 3 (PE3’s Index) | Encoding indexes
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ of PE2 to PE5
4 |0| NodeIndex = 4 (PE4’s Index) | by NodeIndex
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
2 |0| NodeIndex = 5 (PE5’s Index) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|B|<-------- NodeIndex -------->|
Indexes of PE2 to PE5 by NodeIndex:
8 bytes, operations on 4 Node Indexes
Indexes of PE2 to PE5 by string:
4 bytes, operations on 8 bits
Using bitstring is more efficient than using NodeIndex

## Slide 7: Solution 2 Specials: More Efficient Encoding
Page 7
Size 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ Indexes
8 |0|NodeIndex = 102 (PE2’s Index)| of PE2 and PE3
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ by NodeIndex Indexes
6 |0|NodeIndex = 503 (PE3’s Index)| 0 1 2 3 4 5 6 7 of PE2 – PE5
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ by NodeIndex and
4 |1| 1004 | 1 |1|1|0|0|0|0|0|0| flexible bitstring
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|B|<------- StartIndex ------->|<-S-BitString->|<--BitString-->|
Size 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 0 1 2 3 4 5 6 7 401 407 Indexes
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ . . . +-+..-+ of PE2 and PE3
58 |1| 102 | 51 |1|0|0|0|0|0|0|0| . . . |1|0|0| by flex bitstring
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ . . . +-+..-+
4 |1| 1004 | 1 |1|1|0|0|0|0|0|0| Indexes of PE4 and PE5
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ by flexible bitstring
|B|<------- StartIndex ------->|<-S-BitString->|<--BitString-->|
For a tree (i.e., egress nodes of tree), optimal or more efficient encoding is selected and used in MRH wrt space and processing time.
For example, for a tree from PE1 to PE2 – PE5,
if PE1 – PE5 have their indexes 2 – 5 respectively, encoding by flexible bitstring is selected;
If PE1 – PE5 have their indexes 102, 503, 1004 and 1005 respectively, encoding by NodeIndex and flexible bitstring is selected.
Indexes of PE2 and PE3 by string:
54 bytes, operations on 408 bits
Indexes of PE2 and PE3 by NodeIndex:
4 bytes, operations on 2 Node Indexes
Using NodeIndex and bitstring is more efficient than using 2 bitstrings

## Slide 8: Next
Comments
Page 8